## Slide 1: Understanding WiFi-based connectivity from moving vehicles
Ratul Mahajan Microsoft Research | 
John Zahorjan University of Washington | Brian Zill Microsoft Research

## Slide 2: Network access from moving vehicles
Highly attractive, increasing demand
Our long-term goal: Build a network and develop protocols to support vehicles using WiFi
  Cheaper and potentially higher throughput than alternatives
  Opportune time to consider this challenge
This work: Investigate connectivity characteristics between vehicles and base stations
  To understand what applications can be supported and what protocols are suitable

## Slide 3: Characterizing V-to-BS connectivity
1. Interested in the basic nature of connectivity provided by the wireless fabric
  E.g., packet loss variation with vehicle movement
2. Can the predictability of vehicular paths mitigate the impact of a fast-changing environment?
  Deploy a testbed and analyze measurements

## Slide 4: Existing work
Either studies what can be done with existing deployments and protocols
  Current protocols have high overheads that can be easily removed
Or studies controlled environments
  Real environments are very different

## Slide 5: VanLAN: Our testbed
Uses campus vans as moving vehicles
Basestations are deployed on roadside buildings
Currently 2 vans, 11 BSes

## Slide 6: Van deployment

## Slide 7: Studying connectivity sessions and disruptions
Define two types of connectivity sessions to a BS:
  Meta session: from coming in to going out of range
  Mini session: period without disruptions in connectivity
First beacon
Last beacon
No beacon for 2+ secs
Meta session
Mini session
Mini session
10 beacons per sec
Gray period

## Slide 8: Moving vehicles experience gray periods
Session duration (s)
Session length (m)
% of sessions
% of sessions
Meta sessions
Mini sessions
Meta sessions
Mini sessions
Mini sessions are much shorter than meta sessions

## Slide 9: Example gray periods
Seconds from start
Reception ratio
Entry phase
Production phase
Exit phase
Observed behavior does not match earlier observations in controlled environments

## Slide 10: Properties of gray periods
Very frequent in our testbed
Most are short but some even longer than 10s
Do not consistently occur at the same location
Hard to predict reliably using online measurements, e.g., of RSSI, reception ratio

## Slide 11: Implications of gray periods
Supporting interactive or disruption-sensitive applications is challenging
Current WiFi association and handoff model performs poorly

## Slide 12: Historical information can help predict performance at a location
Simulation
Testbed
Past reception ratio
Prediction error in reception ratio

## Slide 13: Historical information can also help identify regions prone to gray periods
Past reception ratio
Prob. of experiencing a gray period

## Slide 14: Conclusions
Moving vehicles frequently encounter gray periods
  Makes it challenging to support some applications
  Minimizing disruptions requires new protocols
Predictions based on past performance at a location can help
More information and data at http://research.microsoft.com/vanlan/