## Slide 1: Bridging centralized programming and distributed control planes
Ryan Beckett | Ratul Mahajan | Todd Millstein | Jitu Padhye | David Walker

## Slide 2: Hypothesis on smart solutions in networks
Infrastructure size or complexity
Total cost
(eng + ops + $/bit)
Simple solutions
Smart solutions
Overprovision, best effort, optimize mean perf, relaxed (distributed) control, ….
Intelligent resource allocation, multiple priorities, optimize tail perf, tight (centralized) control, …
Past
Present

## Slide 3: Network programming journey
 | Distributed programming | Centralized programming
Distributed control plane |  | 
Centralized Control plane |  | 
+ Resilience
− Programmability
Notes: Programmability directly tied to policy compliance and configuration errors

## Slide 4: Programming (configuring) networks is error-prone

## Slide 5: Programming (configuring) networks is error-prone
50-80% of outages are the result of human error
-Juniper 2008
60% of network downtime is caused by human error
-Yankee group 2002

## Slide 6: Network programming journey
 | Distributed programming | Centralized programming
Distributed control plane |  | 
Centralized Control plane |  | 
+ Resilience
− Programmability
+ Programmability
+ Resilience
+ Programmability
− Resilience
Network verification
Notes: Programmability directly tied to policy compliance and configuration errors

## Slide 7: Programming distributed control planes is hard
Peer
Prov
Cust
R1
R2
R3
R4
Network-wide policies
Prefer one neighbor over another
Don’t use my network as transit
Keep traffic within a region
Aggregate prefixes externally
Router-level mechanisms
Set consistent, per-link preferences
Tag incoming routing info
Program import and export filters based on various route attributes

## Slide 8: Propane: Centrally programming distributed control planes
A language for expressing of network-level objectives
Path constraints and relative preferences (fallbacks)
A compiler that configures router-level mechanisms
Configurations are policy-compliant under all failures
Notes: Uniform abstractions for internal and external routing

## Slide 9: Example #1: A backbone network
Peer1
Peer2
Cust
R1
R2
Goals
  No transit between peers
  Prefer R2 > R1 > Peer{1,2}
  Limit Cust to 16.4.0.0/16
block “Peer”
tag “Peer”
block “Peer”
tag “Peer”
LP=100
LP=99
LP=101
filter 16.4.0.0/16
LP=99
filter 16.4.0.0/16
define notransit = {true => not transit({Peer1, Peer2})}
define preference = {true => exit (R2>R1>{Peer1, Peer2})}
define ownership = {16.4.0.0/16 => end(Cust)}
define main = notransit and preference and ownership

## Slide 10: Example #2: A data center network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Y
X
D
C
A
B
E
F
H
G
Y
C
D
A
B
G
H
E
F
Goals
  Keep local prefixes internal
  Aggregate global prefixes as PG
Attempt #1
Don’t export from G, H to external
Aggregate externally as PG
Backbone

## Slide 11: Example #2: A data center network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Y
X
D
C
A
B
E
F
H
G
Y
C
D
A
B
G
H
E
F
Goals
  Keep local prefixes internal
  Aggregate global prefixes as PG
Attempt #1
Don’t export from G, H to external
Aggregate externally as PG
Backbone

## Slide 12: Example #2: A data center network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Y
X
D
C
A
B
E
F
H
G
Y
C
D
A
B
G
H
E
F
Goals
  Keep local prefixes internal
  Aggregate global prefixes as PG
Attempt #2
Don’t export from G, H to external
Aggregate externally as PG
Valley-free routing
PG
Backbone

## Slide 13: Example #2: A data center network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Y
X
D
C
A
B
E
F
H
G
Y
C
D
A
B
G
H
E
F
Goals
  Keep local prefixes internal
  Aggregate global prefixes as PG
Attempt #2
Don’t export from G, H to external
Aggregate externally as PG
Valley-free routing
PG
Backbone

## Slide 14: Example #2: A data center network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Y
X
D
C
A
B
E
F
H
G
Backbone
Y
C
D
A
B
G
H
E
F
Goals
  Keep local prefixes internal
  Aggregate global prefixes as PG
Attempt #2
Don’t export from G, H to external
Aggregate externally as PG
X, Y block routes through the other
PG
PG1 blackholed!

## Slide 15: Example #2: A data center network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Y
X
D
C
A
B
E
F
H
G
Y
C
D
A
B
G
H
E
F
define ownership = {PG1 => end(A),
PG2 => end(B),
PL1 => end(E),
PL2 => end(F)}
define locality = { {PL1, PL2} => always(in)}
control {aggregate(PG, in -> out)}
define main = routing and locality
Goals
  Keep local prefixes internal
  Aggregate global prefixes as PG
Backbone

## Slide 16: Propane compiler
Propane
Regular IR
Product graph
Abstract BGP
Cisco
Juniper
Front End Constraint Language
Regular Expression-based IR
Topology
Failure analyses
Vendor-independent BGP
Vendor configurations

## Slide 17: Propane Regular IR
Propane
Regular
IR
Step 1: Combine modular constraints Prefix-by-prefix intersection of constraints
define ownership = {PG1 => end(A),
PG2 => end(B),
PL1 => end(E),
PL2 => end(F)}
define locality = { {PL1, PL2} => always(in)}
control {aggregate(PG, in -> out)}
define main = routing and locality
PG1 => end(A)
PG2 => end(B)
PL1 => always(in)and end(E)
PL2 => always(in)and end(F)

## Slide 18: Propane Regular IR
Step 2: Expand constraints in to regular expressions
  exit(X) =
  (out*.in+.(X ∩ out).out*)
  (out*.in*.(X ∩ in).out+)|
  any = out*.in+.out*
  end(X) = (Σ*.X)
Step 3: Reduced syntax
  always(X) =
  (X)*
  true => A.(X >> Y).out*
  true => (A.X.out*) >> (A.Y.out*)
  start(X) =
  avoid(X) =
  waypoint(X) =
  (X.Σ*)
  (!X)*
  (Σ*.X.Σ*)
Propane
Regular
IR

## Slide 19: PG construction: An Example
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:
Regular IR
Product graph

## Slide 20: PG construction: An Example
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:
Regular IR
Product graph

## Slide 21: PG construction: Reversed policy automata
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out)
  (W.B.in+.out)
0
1
2
3
4
  in
  B
  W
  ACDE
  B
  ACDE
  out
0
1
2
3
4
5
  out
  D
  C
  A
  W

## Slide 22: PG construction: Graph generation
B
A
D
E
C
Z
Y
X
W
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  in
  B
  W
  ACDE
  B
  ACDE
  {2}
  {1}
start
(Z,1,1)
(W,1,1)
(Y,1,1)
(X,1,1)
(B,-,2)
(A,-,2)
(E,-,2)
(D,2,2)
(C,-,2)
(D,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end
  out
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 23: PG construction: Graph generation
B
A
D
E
C
Z
Y
X
W
0
1
2
3
4
5
  out
  D
  C
  A
  W
  {2}
  {1}
start
(Z,1,1)
(W,1,1)
(Y,1,1)
(X,1,1)
(B,-,2)
(A,-,2)
(E,-,2)
(D,2,2)
(C,-,2)
(D,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end
0
1
2
3
4
  in
  B
  W
  ACDE
  B
  ACDE
  out
  (W.A.C.D.out) >> (W.B.in+.out)
Notes: Compact representation of all paths through the topology subject to policy constraints

## Slide 24: PG construction: minimization (loop analysis)
  {2}
  {1}
start
(Z,1,1)
(W,1,1)
(Y,1,1)
(X,1,1)
(B,-,2)
(A,-,2)
(E,-,2)
(D,2,2)
(C,-,2)
(D,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end
Notes: 6 checks
- 3 for nodes
- not on a simple path
- pre-dominated (from start) by another version of yourself
- post-dominated (toward end) by another version of yourself
-

## Slide 25: Compilation to ABGP
Idea 1: Restrict advertisements to PG edges
  Encode PG state in community tag
  Incoming edges — import filters
  Outgoing edges — export filters
Let BGP find some allowed path dynamically
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end
Product graph
Abstract BGP

## Slide 26: Compilation to BGP
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end
C allows import from D with tag (2,2)
C exports to A,B with tag (3,2)
Product graph
Abstract BGP

## Slide 27: Compilation to BGP
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end
A better path exists in the
network, but is not used!
(W.A.C.D.out) >> (W.B.in+.out)
B
A
D
E
C
Z
Y
X
W

## Slide 28: Compilation to BGP
Idea 2: Synthesize local preferences
Let BGP find the best allowed path dynamically
  Direct BGP towards best path
  Under all combinations of failures
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end

## Slide 29: Compilation to BGP
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end

## Slide 30: Compilation to BGP
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end

## Slide 31: Compilation to BGP
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end

## Slide 32: Compilation to BGP
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end

## Slide 33: Compilation to BGP
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end
choice

## Slide 34: Compilation to BGP
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
choice
Highest preference
obtainable here
But there
could be a
failure!
X

## Slide 35: Compilation to BGP
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end
choice
X

## Slide 36: Compilation to BGP
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
Safe to prefer D
  {2}
  {1}
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(E,-,2)
(D,2,2)
(C,-,2)
(C,3,2)
(B,-,3)
(A,4,2)
(W,-,4)
(W,5,-)
end

## Slide 37: Propane compiler implementation
Efficient graph algorithms
  Minimization
  Failure safety
  Aggregation blackholes
Config minimization
5500 LoC (F#)
Propane
Regular IR
Product graph
Abstract BGP
Cisco
Juniper
Notes: Output Quagga

## Slide 38: Evaluation on Microsoft network policies
Data center networks
31 lines of Propane
9 mins for 1400 routers
Backbone networks
43 lines of Propane
3 mins for 200 routers
Notes:   Implementation has 5500 lines of F#
  Policies translated from English documents

## Slide 39: Summary
Centralized programming of distributed control planes
Resilient and programmable networks
Generates BGP configurations from high-level policies
using a product graph abstraction of control plane
github.com/rabeckett/propane
Propane