## Slide 1: SWAN: Software-driven wide area network
Ratul Mahajan

## Slide 2: Partners in crime
Ratul Mahajan
Chi-Yao Hong
Vijay Gill
Srikanth Kandula
Ming Zhang
Roger Wattenhofer
Harry Liu
Xin Jin
Rohan Gandhi
Mohan Nanduri

## Slide 3: Inter-DC WAN: A critical, expensive resource
Hong Kong
Seoul
Seattle
Los Angeles
New York
Miami
Dublin
Barcelona
Notes: Services need inter-DC WAN for performance and reliability.
100s of Gbps capacity over long distances.
Costs 100s of millions of dollars amortized annually.

## Slide 4: But it is highly inefficient
Notes: Even the busiest links are used 40-60% of the time.

## Slide 5: One cause of inefficiency: Lack of coordination
Notes: Services send when they want and however much they want.
- leads to cycles of over and under-subscription
Poor utilization can be countered by leveraging traffic characteristics.
- some traffic can be delayed
Adapting this traffic will allow a smaller network to carry the same traffic or allow more traffic to be carried over a network.

## Slide 6: Another cause of inefficiency: Local, greedy resource allocation
Local, greedy allocation
A
B
C
D
E
F
G
H
B
C
D
F
G
H
A
E
Globally optimal allocation
[Latency inflation with MPLS-based traffic engineering, IMC 2011]
Notes: Explain MPLS and tunnels.
Sub-optimality was observed in practice. [IMC paper]

## Slide 7: SWAN: Software-driven WAN
Highly efficient WAN
Flexible sharing policies
Coordinate across services
Centralize resource allocation
Goals
Key design elements
[Achieving high utilization with software-driven WAN, SIGCOMM 2013]
Notes: Want network utilization to be upwards of 95% from the current standard of 40-60%
High efficiency alone is trivial to achieve; must support policies.
  Strict priority classes
  Max-min fair within a class

## Slide 8: Software-defined networking: Primer
Networks today
Beefy routers
Control plane: distributed, on-board
Data plane: indirect configuration
SDNs
Streamlined switches
Control plane: centralized, off-board
Data plane: direct configuration
Notes: Beefy routers are expensive
Control logic:
- Distributed means that its inefficient and does not enable direct, flexible control
- On-board means that bugs take a long time to detect and resolve
Streamlined switches:
retain only the forwarding component
Centralized control logic:
Centralized means its direct and flexible
We write it means that we have quickly detect and resolve issues
Network allocation is programmed directly into the forwarding filters

## Slide 9: SWAN overview
SWAN controller
WAN
Service hosts
Network agent
Service broker
Traffic demand
BW allocation
Network config.
Topology, traffic
Rate limiting
Notes: Bandwidth broker represents service hosts. Required for scalability and also allows for service-specific logic and policies.

## Slide 10: Key design challenges
Scalably computing BW allocations
Avoiding congestion during network updates
Working with limited switch memory

## Slide 11: Scalably computing allocation
Goal: Prefer higher-priority traffic and max-min fair within a class
Challenge: Network-wide fairness requires many MCFs
Approach: Bounded max-min fairness (fixed number of MCFs)
Notes: Allocate resources to higher priority traffic first, along shorter paths.
Then allocate lower priority traffic.
Path-constrained, multi-commodity flow (MCF) problem
Faireness is hard because the exact solution requires linearly many MCFs
Solutions exist with fancier search functions that reduce the number of LPs
Our solution offers bounded fairness with provable bounds on the degree of unfairness
Fixed number of iterations

## Slide 12: Bounded max-min fairness
demand
demand
demand
demand
demand
Geometrically partition the demand space with parameters

## Slide 13: Bounded max-min fairness
demand
demand
demand
demand
demand
Maximize throughput while limiting all allocations below

## Slide 14: Bounded max-min fairness
demand
demand
demand
demand
demand
Maximize throughput while limiting all allocations below

## Slide 15: Bounded max-min fairness
demand
demand
demand
demand
demand
Fix the allocation for smaller flows

## Slide 16: Bounded max-min fairness
demand
demand
demand
demand
demand
Continue until all flows fixed

## Slide 17: Bounded max-min fairness
demand
demand
demand
demand
demand
Fairness bound: Each flow is within of its fair rate
Number of MCFs:
Notes: “practice”

## Slide 18: SWAN computes fair allocations
In practice, only 4% of the flows deviate more than 5%
Relative deviation
SWAN ()
Flows sorted by demand
MPLS TE
Relative deviation

## Slide 19: Key design challenges
Scalably computing BW allocations
Avoiding congestion during network updates
Working with limited switch memory
Notes: For scalable computations, we played several other tricks too, which I won’t get into.

## Slide 20: Congestion during network updates

## Slide 21: Congestion-free network updates

## Slide 22: Computing congestion-free update plan
Leave scratch capacity on each link
Ensures a plan with at most steps
Find a plan with minimal number of steps using an LP
Search for a feasible plan with 1, 2, …. max steps
Use scratch capacity for background traffic

## Slide 23: SWAN provides congestion-free updates
Complementary CDF
Oversubscription ratio
Extra traffic (MB)

## Slide 24: Key design challenges
Scalably computing BW allocations
Avoiding congestion during network updates
Working with limited switch memory

## Slide 25: Working with limited switch memory
Notes: Fully using capacity requires using many paths through the network.
Each path needs memory at switches.
Analysis shows:
If we take the demand matrix across time, the number of paths required exceeds the capacity of even next generation switches.
Current generation switches will lead to a big loss in utilization.

## Slide 26: Working with limited switch memory
Install only the “working set” of paths
Use scratch capacity to enable disruption-free updates to the set
Notes: Observation: at any given instant the number of paths required is much smaller.

## Slide 27: SWAN comes close to optimal
SWAN
Throughput
(relative to optimal)
SWAN
w/o rate control
MPLS TE

## Slide 28: Deploying SWAN in production
WAN
Data center
WAN
Data center
Lab prototype
Partial deployment
Full deployment

## Slide 29: Key lesson from using SDNs
Notes: Promise of SDNs:
- You can configure your network just the way you want it
- Direct control can avoid convergence issues of distributed protocols such as loops, drops, and other uncertainties
Reality today:
- Bad things still happen in between stable states
Change is hard
http://blog.richmond.edu/rapmusic/2012/10/20/tricia-rose-on-obama-2/

## Slide 30: Loops in SDNs
Notes: The problem is more general than congestion
Loops.
Avoiding these issues requires careful orchestration of updates.
When a switch can be safely updated depends on whether certain other switches have been updated
This thus introduces dependencies between switches

## Slide 31: Dependencies are worse than you might think

## Slide 32: Ongoing work: Robust, fast network updates
Understand fundamental limits
Develop practical solutions
Notes: We need to understand fundamental limits: what dependencies are really essential.
And we need to develop practical solutions for network updates that are both fast in the presence of stragglers and robust when switch updates fail entirely.

## Slide 33: What are the minimal dependencies for a desired consistency property?
[On consistent updates in software-defined networks, HotNets 2013]

## Slide 34: Network update pipeline
Robust rule generation
Dependency graph generation
Update execution
Routing policy
Consistency property
Network characteristics

## Slide 35: Robust rule generation: Example
Notes: Two questions:
- how to compute?
- how much throughput is lost?

## Slide 36: Robust rule generation
Goal: No congestion if any k or fewer switches fail to update
Challenge: Too many failure combinations
Approach: Use a sorting network to identify worst k failures
  O(kn) constraints

## Slide 37: Robust rule generation: Preliminary results
Chart: Normalized throughput
| max | k/n=10% | k/n=20% | k/n=30% | worst-case
 | 1 | 0.97967 | 0.97738 | 0.97664 | 0.60736

## Slide 38: Network update pipeline
Robust rule generation
Dependency graph generation
Update execution
Routing policy
Consistency property
Network characteristics

## Slide 39: Dependency graph generation
A
Del @
A
Add @
Del @
Del @

## Slide 40: Update execution
Updates without parents can be applied right away
Break any cycles and shorten long chains
A
D
A
A
D
D
Add @

## Slide 41: Update execution: Preliminary results

## Slide 42: Summary
SWAN yields a highly efficient and flexible WAN
  Coordinated service transmissions and centralized resource allocation
  Bounded fairness for scalable computation
  Scratch capacities for “safe” transitions
Change is hard for SDNs
  Need to understand fundamental limits, develop practical solutions
Notes: We set out to build a wide area network that was highly efficient, raising efficiency from the current levels of under 50% to over 95%.
We realized that the current inefficiency stems from services sending in an uncoordinated manner,
- Drove the network from periods of extremely high usage to periods of low usage.
The opportunity was to fix this by coordinating when and how much services send, thus flattening the overall utilization curve, and filling the valleys with low priority traffic.
In realizing this architecture, we had to address several challenges.